## Slide 1: Infrastructural and Community Resilience on the Coast: Lessons Learned from Recent Hurricanes
James M. Kaihatu
Zachry Department of Civil Engineering
Texas A&M University
College Station, TX

## Slide 2: Corpus Christi, TX

## Slide 3: Historical Storms
Year | Storm Name | Category at Landfall
1916 | Hurricane | 4
1919 | Florida Keys Hurricane | 3
1961 | Carla | 4
1967 | Beulah | 3
1970 | Celia | 3
1978 | TS Amelia | NA
1980 | Allen | 3
1999 | Bret | 3
2017 | Harvey | 3-5
Source: Wikipedia

## Slide 4: Hazard: Storm Intensity
Kossin et al., GRL v. 34, 2007

## Slide 5: Hazard: Sea Level Rise

## Slide 6: Adaptability to Increasing Hazard
Mexico Beach, January 2016
Mexico Beach, November 2018
Rebuild?
Or adapt?
Aftermath of Hurricane Michael

## Slide 7: Hurricane Ike
West of Landfall
East of Landfall
Foundation Failure
Severe Road Damage
Intermittent Structural Damage
Evidence of High Surge and Wave Damage
Functional Road
Same storm
Different damage types
Different design criteria
Source for Wind Field Figure: NOAA

## Slide 8: Hurricane Ike
Clear Lake Marina
Galveston Boat Basin
Bolivar Boat Basin
Floating Docks
Metal Roof with Wooden Trusses
Metal Roof with Metal Rafters
Local Slip Damage
Boat Damage
Metal Roof with Wooden Rafters
Widespread Damage to Slips
Missing Roof

## Slide 9: Hurricane Harvey
Source: dallasnews.com

## Slide 10: Hurricane Michael
Slab on grade beachfront?
Wave Damage
Likely Surge Level
Nearby House
Slightly Higher Elevation
Failed Prestressed Concrete Piles
Watertight Modular Home
Mix of older structures (weaker codes) and new, stronger structures
Mix of types of construction (wood/concrete)
Notes: Wave damage

## Slide 11: Hurricane Michael
Panama City Marina
St. Andrews Marina
Laid Back Boat Marina
Marina Landing Harbor
Boats racked against bridge by return current
Concrete piers and metal roof
Sheet metal roofing
Most slips ok
Floating docks and concrete piers
Gulf
Several “rogue” ships
Large “rogue” ship with bad lines
Wooden bollards and docks
Heavy slip damage
Fiberglass covered steel piles
Vinyl piers
Many slips in good shape

## Slide 12: Lessons Learned
Residential Areas
  Elevation is key
  Concrete >> wood (but may not be enough?)
  Adaptation is key ingredient to resilience
  Uniform code enforcement and retrofitting of old structures essential
  More than a single type of failure for each storm
Marinas
  Design for all phases of a storm
  Concrete >> wood
  Enforce requirements on lines
  Floating docks?
  As much geotechnical issue as structural (pile foundations)

## Slide 13: Coastal Engineering Design for Resilience
Gray vs. Green Engineering
Planned Communities for Coastal Resilience
Harbor and Marina Design for Resilience
Probabilistic Design for Multi-Hazards

## Slide 14: Traditional: Gray Engineering
Sources: Wikipedia, CBI-TAMUCC, Houston Chronicle, USACE
Westchester, New York
Poorly designed groins
Breach in barrier island
Beach fill placed by USACE
Existing groins
Notes: Galveston Seawall: Gray engineering
Does what it is supposed to
Exacerbates erosion of beaches
Breakwaters

## Slide 15: “Green Engineering” – Use Natural Resources Available
“The best nature based solution is one that already exists” – I. Losada
“Going green is difficult as there is little quantitative design information…” – R. Dalrymple, NAE
Careful design and testing required!

## Slide 16: “Green Engineering” – Smaller Engineering Footprint
Beach dunes enforced with sand filled “geotubes”
Construction of dunes anchored by vegetation
Careful testing required! (some installations problematic for Ike)
Careful testing required! (vulnerable to problems from incomplete analysis)
Source: New Jersey Sea Grant, coastalcare.org

## Slide 17: Planned Communities for Coastal Resilience – Mix of Gray and Green
Dune construction and vegetation for surge suppression
Reefs or Submerged Structures for wave dissipation
Hardened structures for surge and wave protection – first line of defense
Optimize for sheltering
New materials need careful testing and analysis

## Slide 18: Harbor and Marina Design for Resilience
Reinforced Concrete piles
Floating concrete docks
Improved Foundation Design
Design for water levels, waves, and current speeds / direction
Careful testing and analysis required!

## Slide 19: Probabilistic Design for Multihazards
Single Hazard Condition as Input
Design Procedure
Resulting Design
Traditional Design Methodology
Range of Conditions within Design Life
Run Design Methodology for Many Conditions
Risk of Failure from Different Conditions over Design Life
Keen and Lynett (2018 ICCE)

## Slide 20: Community Resilience
Hazard
Movement toward “Normal”
Hazard
Hazard
Hazard
Storm Intensity
Sea Level Rise

## Slide 21: Final Thoughts
Bad news
  Hazards are increasing in intensity
  Hazards are complex, eludes “one size fits all” approach
  Sea level rise adds to design uncertainty over design life
Good news
  Judicious mix of green and gray engineering / new materials can help
    Requires careful design and testing / analysis
  More is known about hazards – can help in design
  Probabilistic design: Accounts for hazard type / variability
    Design to the hazard, not just the water level
Caution
  Don’t just rebuild – adapt!
  Community involvement is key

## Slide 22: Thanks!
Adapt!
Ike 2008
Post-Ike 2009
Ike 2008
Post-Ike2009
Adapt??
Scour
Mini-dune!!
Beachfront
New housing, further from shore

## Slide 23: Further Information
James M. Kaihatu, Ph.D.
Professor
Associate Department Head for Research
Zachry Department of Civil Engineering
Texas A&M University
3136 TAMU
College Station, TX 77843-3136
979-862-3511 / 979-845-1353
jkaihatu@tamu.edu
Web: https://ceprofs.civil.tamu.edu/jkaihatu
Twitter: @TAMU_Coastal
YouTube: James Kaihatu (link, or enter in search field)